48 Cubic Inch Modified Class Rules

- Engine block must be cast iron. Super Cub Stock Altered Block allowed. (NO Jones & NO Wolam)

- Head bolt pattern must remain in factory form and location.

- Intake and exhaust ports must remain in factory location.  No reversing ports. (Can not be cut off and rewelded in different location or angle).

- Welding and epoxy may be used on outside of block for repairs and stability.

- Maximum displacement 48.00 cubic inch.  Single cylinder engine.

- One carburetor with single venturi.

- 1050 lbs. and 8 ft. weight bar.

- Maximum tire size is 26x12x12.

- 48 cubic inch modified will be allowed to pull with Pro-Stock using 48 c.i. carb. if there are two or less tractors in the 48 or Pro-stock class making it a mix class.

- Fuel being alcohol (NO ADDITIVES-CLEAR).  Fuel must remain essentially clear during water test.  Fuel can also be checked via Hydrometer-796 true specific gravity maximum reading at 60 degrees Fahrenheit with conversion chart used to determine equivalent at other temperatures.

- Fuel being gasoline see stock rules.

- Maximum wheel base is 56” centerline to centerline, no tube frames.

- Head hold down required.

- Guards – Flywheel top and bottom, engine guard opposite side of can must be attached top and bottom.  All guards are to be 1/8 in. steel or 3/16 aluminum minimum.  Factory sheet metal sides is not acceptable, must have additional metal attached to meet minimum requirements.

- 48 cube are allowed to run with PRO (Midwest Super Cub Rules)

- The weight bar, brackets of weights cannot extend more than 8’-0” from the center of the rear axle to the most forward point.

- A fire extinguisher is required on all alcohol running tractors.

- The kill switch must kill the fuel pump on modified tractors.