- Tractor must have a stationary hitch, with a minimum 3/8”, maximum ¾” thickness.  Only one hitching point on a tractor and/or second hitch must be plugged.  Minimum opening for hook is 1 ½ inches.  Maximum drawbar height is 13 inches.  Height is checked at the highest point the hook contacts hitch.  Hook point of drawbar must not be less than 6 inches from centerline of rear axle and not inside the plane of the differential cover plate.

- All weights must be securely fastened and cannot be moved while in motion.  Weights at rear of tractor must not extend beyond rear tires.  Tractor weight and hitch height will be checked as they are in pulling position. Tractor must be weighed and hitch height checked with the driver seated on the tractor before each pull. Tractors may be spot checked after each pull.  During a spot check, a maximum of 2 lbs. over class weight is allowed for the build up of dirt.  Hitch must clear height checker.

- In the 8, 12, 16 hp stock classes weight bar, brackets, or weights can not extend more than 6’-6” ft. from center of rear axle to most forward point.

- All exhaust must discharge vertical. Factory garden tractor type tires may be cut.  No dual wheels, steel lugs, slicks, chains, four-wheel drive, locked or welded rear ends, mower decks, and/or foreign materials or resin, etc.

- No part of tractor can interfere with hook.  The chain can not touch any part of tractor when hooked and pulled tight.

- Stock classes must use stock frames. They may have minor alterations. The maximum wheel center to center distance is 52”. No homemade frames or cut on frames that would change length or width of OEM.  Flywheel clearance accepted.  Engine need not be horsepower or make for the frame it is used in.

- All tractors must have a working kill switch with ring or loop a minimum of one inch in diameter mounted on the rear of the tractor in accessible position for sled hookup. It is the responsibility of the drivers to locate the switch so that the rope will not tangle with the rear of the tractor.

- All tractors must have full hoods securely fastened, fenders, adequate steering, and workable brakes.

- All tractors will have a 3 in. tall (high) seat back or equivalent (not 3 in. long).  It must be 60% of seat width and sturdy.

- All fuel tanks must be securely fastened and have a proper cap.  All fuel line connections must be securely fastened (crimped, clamped, flared, etc.). Fuel must comply with class rules. Random checks may be made at any time by officials.

- All clutches, belts, drive pulleys, u-joints, flex coupling, etc. must be covered 360 degrees including the length of the device with a minimum of 3/16” aluminum, 1/8” steel or equivalent, subject to class rules.  Start pulleys must have adequate bolt and washer screwed in the end of the crankshaft to retain a loose pulley.

- All tractors must have a side shield opposite camshaft side of motor to contain debris in case of engine failure.  Minimum dimension are from bottom of engine to 4 ½” above the center line of crankshaft, by 7” in width, with a minimum of 3/16” aluminum, 1/8” steel or equivalent, centered over block and securely fastened to the frame of tractor and at the top.  Blankets or other shields are encouraged.

- Factory side sheet metal is not acceptable for guard.  You may line the inside of side cover with metal or aluminum to meet requirements.

- All tractors must have a dead man throttle with forward motion to accelerate (spring return).

- All tractors running over 4000 RPM must have a steel flywheel.  No exception.

- All tractors must have rear anti-turnover devices sufficient to support weight of tractor.  A minimum of two metal centered wheels, 5” in diameter and 1” wide, or two steel pads not less than 3” square must be used.  The bottom of the wheels or pads must be 5” or less above the ground and at least 5” from back of rear tires to the center of wheels of pads.  (¼” variance maximum on these 2 measurements only).  Tech Official will make final decision.

- Tractors can run an electric fuel pump. The electric fuel pump must be wired in with the kill switch and the tractor must be equipped with a fire extinguisher.